RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 466 – fire resistant louvre

Manufacture and reference :

The 466 is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 466 is a fire resistant louvre. It holds its integrity and thermal insulation for one hour (EN13501-2).

System operation and Airflow Performance:

Type				466

Visual Free Area		70%

Physical Free Area		70%

K-factor: Intake			6.8

K-factor: Discharge		6.8

Ce coefficient: Intake		0.383

Cd coefficient: Discharge	0.383

Dimensions/Size Range:

Pitch (mm)			20

Product Construction:

Outerframe: Extruded aluminium (EN 12020-2)

Blades filled with intumescent material

Surface Treatment:

Outerframe: sation anodised (20 microns)

Other frame colours on request

Installation:

It is designed to be built-in internally only.

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html