specification sheet

ar45

window ventilation – NON-adjustable supply

manufacturer

RENSON Ventilation, IZ 2 Vijverdam, Maalbeekstraat 10, 8790 Waregem – Belgium

tel. +32 (0)56 62 71 11, fax. +32 (0)56 60 28 51, info@renson.be  www.renson.eu

series

self-regulating

non-thermally broken

window ventilation

for installation on glass

types

AR45 for glass thickness 20mm

AR45 for glass thickness 24mm

AR45 for glass thickness 28mm

description

The AR45 is a compact, self-regulating non-thermally broken window ventilator.

The AR45 is designed for installation on glass (for glass thicknesses 20, 24, 28 mm), in wooden, PVC and aluminium windows.

The airflow is regulated by means of an aluminium flap on the inside. When open, it deflects the airflow upwards to prevent direct draughts.

The AR45 contains maintenance-free, self-regulating elements that react automatically to pressure differences and wind strengths, and cannot be controlled by the user.

The extruded aluminium base profile consists of one profile with 9.4 x 35 mm perforations to let the air through.

A glazing gasket is recommended to guarantee a perfect fit.

Operating the unit is not possible - the inside flap is open permanently.

The finish can be anodised (natural) or powder-coated (any RAL colour).

The end caps are in white or black technical plastic (ASA Luran S).

material & finish

Internal and external profile: AlMgSi 0.5 aluminium

Finish: natural (E6/EV1-SAA) anodising (20 micron) or powder-coating (60-70 micron) in all RAL colours

End caps: ASA polymer type Luran S (colour-fast, weather- and UV-resistant)

End cap colours: white, black, other colours upon request

dimensions

Glass reduction: 	45 mm

Height:			58 mm

Max. length: 		2500 mm

control options

Operating the unit is not possible

Technical specifications

Airflow:

- Q at 1 Pa:		14,6 m³/h/m (4,1 l/s/m)

- Q at 2 Pa: 		21,4 m³/h/m (5,9 l/s/m)

- Equivalent Area:	5161 mm²/m

Sound reduction Dn,e,w (C;Ctr):

- Open:	27 (0;0) dB

- Closed: 	44 (0;0) dB

Self-regulation class: 	non-self-regulating: P0

U-value: 			- W/m²K

Watertightness up to: 		350 Pa (closed)

Windtightness up to: 		350 Pa (closed)

standards

This product is manufactured according to, complies with and/or has been tested according to:

EN ISO 140-10

EN ISO 717-1

EN 1026

EN 1027

EN 13141-1

EN 12020-2

EN AW 6063 T66

NBN D50-001

EN 1077-2