SPECIFICATION SHEET

sonovent® V

ACOUSTIC WINDOW VENTILATION - ADJUSTABLE SYPPLY

MANUFACTURER

RENSON Ventilation, IZ 2 Vijverdam, Maalbeekstraat 10, 8790 Waregem – België

tel. +32 (0)56 62 71 11, fax. +32 (0)56 60 28 51, info@renson.be  www.renson.eu

series

non-self-regulating

thermally broken

noise dampening

mechanical

window ventilation

for installation at transom

types

SONOVENT® V SMALL,  supply, glass thickness 20 mm

SONOVENT® V SMALL,  supply, glass thickness 24 mm

SONOVENT® V SMALL,  supply, glass thickness 28 mm

SONOVENT® V SMALL,  supply, glass thickness 32 mm

SONOVENT® V SMALL,  supply, glass thickness 20 mm

SONOVENT® V SMALL,  supply, glass thickness 24 mm

SONOVENT® V SMALL,  supply, glass thickness 28 mm

SONOVENT® V SMALL,  supply, glass thickness 32 mm

DESCRIPTION

The SONOVENT® V is a thermally broken and mechanical (24V) window ventilator (supply and extraction) with an airflow of 220 m³/h/m, a good level of noise reduction and has been designed for installation at transom. Two versions of the SONOVENT® are available: one for extraction and one for the supply of fresh air.

The ventilator starts operating automatically when the aluminum flap within the device is opened. The SONOVENT® V can be operated manually, by rod, by chord or by motor. With each type of control, the interior flap is operated in a continuous way.

the ventilator can be used to supply fresh air or extract polluted air (cannot be used in order to extract moist and polluted air from bath rooms or kitchens). The mechanical parts can be disassembled from the inside. 

The interior profile has a double row of perforations of 3 × 22 mm that functions as an insect mesh. The perforated interior profile is removable for cleaning purposes. 

the SONOVENT® V has been designed for installation at transom and this for glass thicknesses of 20, 24, 28, 32 mm. Other glass thicknesses are available on demand. The height of the flanges (both bottom and top) is 25 mm. 

Noise insulation is ensured through the application of non-flammable mineral wool inside the SONOVENT® V. 

The client can chose the position of the thermal bridge (three possible positions for the Small version).

A powder coated (all possible RAL colours) and dual color finish is possible.

material & finish

Internal and external profile: aluminium AlMgSi 0.5

Finish: powder-coating (60-70 microns) in all possible RAL colours (dual color possible)

Thermal bridge: PVC

End caps: ASA polymer type Luran S (colour-fast, weather- and UV-resistant)

End cap colours: black or white

Noise-dampening material: non-flammable mineral wool

dimensions

Glass reduction: 		135 mm

Height:				105 mm

Total height with flanges :	155 mm

Height flange:			25 mm

Maximal length: 		2500 mm

Minimal length:			500 mm

Depth:				170 mm

Total Depth :			205 mm

controls

Manual operation, continuous adjustment

Cord control, continuous adjustment

Rod control,  continuous adjustment

Motorised operation, 24V DC, continuous adjustment

technical specifications

sonovent® V SMALL, supply

Airflow:

- Q: 		220 m³/h/m

Noise reduction Dn,e,w (C;Ctr):

- In open position:	35 (-1;-3) dB

- In closed position: 	n.g. dB

Self-regulating:	 		not applicable

U-value: 			4,5 W/m²K

Watertightness up to: 		650 Pa (closed position)

Airflow leakage at 50 Pa:	not applicable

sonovent® V SMALL, extraction

Airflow:

- Q: 		220 m³/h/m

Noise reduction Dn,e,w (C;Ctr):

- In open position:	35 (-1;-3) dB

- In closed position: 	n.g. dB

Self-regulating:	 		not applicable

U-value: 			4,5 W/m²K

Watertightness up to: 		650 Pa (closed position)

Airflow leakage at 50 Pa:	not applicable

standards

This product is manufactured according to, complies with and/or has been tested according to:

EN ISO 140-10

EN ISO 717-1

EN 1026

EN 1027

EN 13141-1

EN 12020-2

EN AW 6063 T66

NBN D50-001

EN 10077-2

DIN 16491