RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 461AK Silendo – acoustic door grille

Manufacture and reference :

The 461AK Silendo is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 461AK Silendo is an acoustic door grille.

System operation and Airflow Performance:

Type				461AK Silendo

Visual Free Area		27%

Physical Free Area		27%

K-factor: Intake			6.1

K-factor: Discharge		6.1

Ce coefficient: Intake		0.4

Cd coefficient: Discharge	0.4

Sound reduction Dn,e,w (C;Ctr)	32 (0 ;-2) dB

Dimensions/Size Range:

Minimum Dimensions (mm)	425(l) x 48(h)

Thickness (mm)		37 to 43

Product Construction:

Profile: Extruded aluminium (EN 12020-2)

Sound absorbing material: synthetic foam

End caps: Luran S ASA polymer

Surface Treatment:

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion to guarantee.

Installation:

It is designed to be built into internal, residential doors.

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html