RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 464 Incendo – fire resistant louvre

Manufacture and reference :

The 464 Incendo is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 464 Incendo is a fire resistant louvre. It holds its integrity and thermal insulation for one hour (EN13501-2).

System operation and Airflow Performance:

Type				464 Incendo

Visual Free Area		61%

Physical Free Area		51%

K-factor: Intake			10.3

K-factor: Discharge		10.3

Ce coefficient: Intake		0.312

Cd coefficient: Discharge	0.312

Dimensions/Size Range:

Minimum Dimensions (mm)	100 x 100

Product Construction:

Outerframe: Polystyrene

Blades filled with intumescent material

Surface Treatment:

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion to guarantee.

Installation:

It is designed to be built internally only.

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html