RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 445/86 – BUILT-IN 60mm pitch wall louvre

Manufacture and reference :

The 445/86 Louvre Panel is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 445/86 is an extruded acoustic aluminium louvre panel using a L.060 AC pitch blade mounted into an integrated frame. It is designed to be built into a pre formed opening.

System operation and Airflow Performance:

Acoustic Performance – Sound reduction index

| Frequency Band | 125 | 250 | 500 | 1000 | 2000 | 4000 |
| --- | --- | --- | --- | --- | --- | --- |
| R (dB) | 5.8 | 1.5 | 1.6 | 4.5 | 9.9 | 10.8 |

Rw (dB): 6 (-1;-2)

Type				445/86

Visual Free Area		77%

Physical Free Area		34%

K-factor: Intake			9.22

K-factor: Discharge		13.29

Ce coefficient: Intake		0.329

Cd coefficient: Discharge	0.274

Dimensions/Size Range:

Minimum Dimensions (mm)	300 x 300

Flange Height (mm)		40

Depth (mm)			150

Pitch (mm)			60

Product Construction:

Profile: Extruded aluminium (EN 12020-2)

Sound absorbing material: inorganic mineral wool

Surface Treatment:

Mill finish

Anodised (EV6/EV1) (20 micron): pre-treated and anodised.

Polyester powder coating in any RAL colour (40 micron): aluminium profiles pre-treated to resist corrosion (DIN 5002155) to guarantee.

Installation:

To be built into a reveal. Reinforcing structure required for panels larger than 3m2.

Accessories

Stainless steel birdguard 6mm x 6mm secured to the rear

Stainless steel insect mesh 2.3mm x 2.3mm secured to the rear

Backframe, pre-installation frame, water channel, drainage channel

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html