RENSON LOUVRE SPECIFICATIONS

Brand		: LOUVRE PANEL

Type 		: 465 – fire resistant louvre

Manufacture and reference :

The 465 is manufactured and supplied by Renson Fabrication Ltd.  Tel: 01622 754123

Email: louvres@rensonuk.net Website: www.renson.eu

Description:

RENSON 465 is a fire resistant louvre. It holds its integrity and thermal insulation for one hour (EN13501-2).

System operation and Airflow Performance:

Type				465

Visual Free Area		74%

Physical Free Area		57%

K-factor: Intake			10.3

K-factor: Discharge		10.3

Ce coefficient: Intake		0.312

Cd coefficient: Discharge	0.312

Dimensions/Size Range:

Minimum Dimensions (mm)	200 x 200

Pitch (mm)			17.5

Product Construction:

Outerframe: Extruded aluminium (EN 12020-2)

Blades filled with intumescent material

Surface Treatment:

Outerframe: sation anodised (20 microns)

Other frame colours on request

Installation:

It is designed to be built-in internally only.

Product Information:

http://www.rensonuk.net/Louvres-panels-United-Kingdom.html