## Specifications sheet

Finishing 
» Electrically plated 10 microns Fe Zn 12 C 

Description 
» Standard sizes. !Frame profiles with a total height of 41,5 mm cut at mitre of 45°. 
» The Z-shaped blades with a height of 50 mm are fixed in the frame by means of 
point welding. 
» The pitch of the blades is 34 mm. 
» An insect screen of 1 mm guage galvanised steel is fitted as standard - square 
screening 12 X12 mm. 

Specification 
» Depth to fit: 43 mm 
» Total thickness: 50 mm 
» Flange size: 40 mm 
» Visual free area: 68% 

Fixing 
» Fixing by means of dowels.